## Slide 1
🫀
rPPG Vital Signs Monitor
How a webcam and a small sensor can measure your heartbeat
Heart Rate
SpO₂
Blood Pressure
Temperature
Respiratory Rate
For secondary school students · Live demo included
1 / 8

## Slide 2
What are Vital Signs?
These are the basic measurements that tell doctors if your body is working properly.
❤️
Heart Rate
How many times your heart beats per minute
Normal: 60 – 100 BPM
🩸
Blood Oxygen
How much oxygen is carried in your blood
Normal: 95 – 100 %
💉
Blood Pressure
The force of blood pushing against artery walls
Normal: < 120 / 80 mmHg
🌡️
Temperature
Your body's internal heat level
Normal: 36.1 – 37.2 °C
🫁
Respiratory Rate
How many breaths you take per minute
Normal: 12 – 20 br/min
2 / 8

## Slide 3
What is rPPG?
Remote PhotoPlethysmoGraphy — measuring pulse without touching you
💡 The simple idea
1. Every heartbeat pumps blood through your face
2. More blood = slightly redder skin colour
3. A camera takes ~15 photos per second
4. A computer detects the tiny colour changes
5. Count the changes → Heart Rate!
Your eye cannot see this change. The camera can! 📷
✅ What rPPG can measure
• Heart Rate
• SpO₂ (estimate)
• Respiratory Rate
• Blood Pressure (estimate)
❌ What rPPG cannot replace
• Clinical-grade blood pressure
• ECG / heart waveform
• Blood glucose level
3 / 8

## Slide 4
The Hardware
Two small devices that work together to read your vital signs
⚙️ ESP32 DevKit
The brain of the system
✦ A tiny computer chip (like a mini PC)
✦ Connects to WiFi to send data
✦ Reads data from the MAX30100 sensor
✦ Sends vital signs to your browser
✦ Costs about RM 15–25
💡 MAX30100 Sensor
The finger sensor
✦ Shines red + infrared LED onto your finger
✦ Measures how much light bounces back
✦ More blood = less light reflected
✦ Detects Heart Rate and SpO₂
✦ Costs about RM 8–15
4 / 8

## Slide 5
How to Connect the Hardware
Just 4 wires from the MAX30100 to the ESP32
MAX30100 Pin
→
ESP32 Pin
Purpose
VIN
→
3.3V
Power supply
GND
→
GND
Common ground
SDA
→
GPIO 21
Data line (I2C)
SCL
→
GPIO 22
Clock line (I2C)
⚠️ Use 3.3V — NOT 5V. The MAX30100 can be damaged by 5V.
I2C = a communication protocol that lets two devices talk using just 2 wires (SDA + SCL)
5 / 8

## Slide 6
How the System Works Together
Three parts talking to each other over WiFi
🖥️
Your Webcam
Captures your face ~15 frames/sec
⚙️
FastAPI Server
Python backend Runs on your PC
📱
Browser Dashboard
Shows all vitals Live updates
→
→
💉
ESP32 + MAX30100
Finger sensor · sends via WiFi HTTP POST
↑ WiFi
Video frames (WebSocket)
Vitals data (WebSocket)
6 / 8

## Slide 7
Live Demo — Try It Yourself!
Follow these steps in order
1
Open the browser
Go to http://172.20.10.3:8090
2
Allow camera access
Click 'Allow' when the browser asks for camera
3
Look at the camera
Keep your face in the green box on screen
4
Place finger on sensor
Gently rest fingertip on the MAX30100
5
Wait ~10 seconds
Numbers will stabilise — that's your heart rate!
7 / 8

## Slide 8
What Did We Learn?
🫀
rPPG uses a camera to detect your pulse
The camera sees tiny colour changes in your skin caused by blood flow
💡
No contact needed for heart rate
Just look at the camera — technology does the rest
⚙️
ESP32 + MAX30100 adds accuracy
The finger sensor gives a more reliable reading alongside the webcam
📊
Estimates vs clinical measurements
rPPG gives good estimates but is not a replacement for hospital equipment
🔮
The future of health monitoring
Smartwatches, phones and laptops may soon measure vitals automatically
8 / 8